## Slide 1: Water
Dr. Bharati Choudhari
Asst. Professor- S&H
KJSCE, SVU,
Vidyavihar.

## Slide 2
Introduction
1). Like air, water is one of the few basic materials which is of prime importance for the preservation of life on this earth.
2). All are aware of the uses of water for drinking, cooking, cooking, bathing & for farming etc.
3). But few know the importance of water as an engineering material.
4). As an engineering material water is used for producing steam, in boilers to generate hydro-electric power, furnishing steam for engines, for construction of concrete structures for manufacturing purposes & as a solvent in chemical process.

## Slide 3
Sources of Water:
The Main Sources Of Water Are:
1). Rain water
2). River water
3). Spring or well water
4). Sea water

## Slide 4
Types of impurities in water:
The impurities present in water are classified as:
1). Dissolved impurities: dissolved impurities may organic or inorganic.
Inorganic impurities: the carbonates, bicarbonates, sulphates, chlorides of calcium, magnesium, iron potassium and aluminium.
Organic impurities: Organic water products, amino acids, proteins, etc. Gases: O2, CO2, Oxides of nitrogen and sulphur, H2S etc.

## Slide 5
2). Suspended impurities: It is of two types:
Inorganic- sand & clay;
Organic- vegetable and animal matter.
3) Biological Impurities: Micro-organisms like pathogenic bacteria, fungi, algae, etc.

## Slide 6
DISADVANTAGES OF HARDWATER/ CAUSES OF HARDNESS:
The following are the disadvantages when hard water is used for various purpose:
DOMESTIC USE:
Washing and Bathing: Hard water does not form lather easily with soap, so soap is wasted
(b) Drinking: Hard water causes bad effects on our digestive system. Sometimes, stone formation takes place in kidneys

## Slide 7
(c) Cooking: The boiling point of water is increased due to the presence of salts. Hence, more fuel and time are required for cooking.
(ii) INDUSTRIAL USE:
Textile Industry: Hard water causes wastage of soap. Precipitates of calcium and magnesium soap adhere to the fabrics and cause problem such difference in color shades, dull shades, patches, etc.
Paper Industry: Calcium and Magnesium salts in water may affect the quality of paper.

## Slide 8
(c) Sugar Industry: Water containing sulphates, carbonates, nitrates affects the crystallisation of sugar.
(d) Pharmaceutical Industry: Hard water may form some undesirable products while preparation of pharmaceutical products.

## Slide 9
(iii) STEAM GENERATION IN BOILERS: For steam generation, boilers are employed. If hard water is used in boilers, It may lead to the following troubles-
Boiler Corrosion
Scale and Sludge formation.
Priming and Foaming
Caustic embrittlement Pharmaceutical industry

## Slide 10
HARDNESS OF WATER (OR) HARDWATER AND SOFT WATER:
Hard Water: The water which does not produce lather (or) very little lather with soap is called Hard Water.
Soft Water: Soft water readily produces a lot of lather when mixed with little soap.
The Hardness of water is caused by the presence of dissolved salts such as Bicarbonates, Sulphates, Chlorides and Nitrates of bivalent metal ions like Ca+2 & Mg+2.

## Slide 11
Soap is sodium/ potassium salt of higher fatty acids like stearic, oleic and palmetic acids. When soap is mixed with soft water lather is produced due to stearic acid and sodium stearate.
Na – Stearate + H2O  NaOH + Stearic Acid
[C17H35COOH]
Stearic Acid + Na-Stearate  Formation of lather.

## Slide 12
When soap comes in contact with HARD WATER, Sodium stearate will react with dissolved calcium and magnesium salts and produce calcium stearate or magnesium stearate which is white precipitate.
2Na– Stearate + Ca+2  Ca– Stearate↓ + 2Na+
[2C17H35COONa] + Ca+2  [(C17H35COO)2Ca]↓ + 2Na+ (Soap) (Soluble) (Insoluble) (Soluble)
[2C17H35COONa] + Mg+2  [(C17H35COO)2Mg]↓ + 2Na+ (Soluble) (Soluble) (Insoluble) (Soluble)

## Slide 13
TYPES OF HARDNESS
The hardness of water is of two types-
Temporary hardness (or) Carbonate hardness
Permanent hardness (or) Non-Carbonate hardness
(1) Temporary Hardness: Temporary hardness is caused by two dissolved bicarbonate salts Ca(HCO3)2 and Mg(HCO3)2. The hardness is called “Temporary Hardness” because it can be removed easily by means of boiling.
Ca(HCO3)2 + Heating  CaCO3↓ + H2O + CO2↑ Mg(HCO3)2 + Heating  Mg(OH)2↓ + 2CO2↑

## Slide 14
(2) Permanent Hardness: Permanent hardness of water is due to the dissolved chlorides, sulphates and nitrates of calcium and magnesium. These salts are CaCl2, CaSO4, Ca(NO3)2, MgCl2, MgSO4, Mg(NO3)2. These hardness cannot be removed easily by boiling. Hence it is called “Permanent Hardness”. Only chemical treatment can remove this hardness.
Total Hardness Of Water = Temporary Hardness + Permanent Hardness

## Slide 15
DEGREE OF HARDNESS:
• The Concentration of hardness as well as non-hardness constituting ions are, usually expressed in the term of “Equivalent amount of CaCO3”
• Since this mode permits the multiplication and division concentration, when required.
• The choice of CaCO3 in particular is due to its molecular weight (m.wt.) is “100” (Equivalent wt. = 50), and
• Moreover, it is insoluble salt that can be precipitated in water treatment.

## Slide 16
Therefore, 100 parts by weight of CaCO3 hardness must be equivalent to-
162 parts by weight of Ca(HCO3)2 hardness
146 parts by weight of Mg(HCO3)2 hardness
136 parts by weight of CaSO4 hardness
111 parts by weight of CaCl2 hardness
164 parts by weight of Ca(NO3)2 hardness
120 parts by weight of MgSO4 hardness
95 parts by weight of MgCl2 hardness
148 parts by weight of Mg(NO3)2 hardness

## Slide 17
Salt | Molar Mass | Chemical Equivalent | Multiplication Factor
Ca(HCO3)2 | 162 | 81 | 100/ 162
Mg(HCO3)2 | 142 | 73 | 100/ 142
CaSO4 | 136 | 68 | 100/ 136
FeCl2 | 127 | 63.5 | 100/ 127
CaCl2 | 111 | 55.5 | 100/ 111
MgSO4 | 120 | 60 | 100/ 120
MgCl2 | 95 | 47.5 | 100/ 95
CaCO3 | 100 | 50 | 100/ 100
MgCO3 | 84 | 42 | 100/ 84
CO2 | 44 | 22 | 100/ 44
Ca(NO3)2 | 164 | 82 | 100/164
Mg(NO3)2 | 148 | 74 | 100/ 148
HCO3- | 61 | 61 | 100/ 122
OH- | 17 | 17 | 100/ 34
CO32- | 60 | 30 | 100/ 60

## Slide 18
Salt | Molar Mass | Chemical Equivalent | Multiplication Factor
NaAlO2 | 82 | 82 | 100/ 164
Al2(SO4)3 | 342 | 57 | 100/ 114
FeSO4.7H2O | 278 | 139 | 100/ 278
H+ | 1 | 1 | 100/ 2
HCl | 36.5 | 36.5 | 100/ 73
The method of calculating degree of hardness is given by the following formula
•Hardness causing salt in terms of equivalent of CaCO3= (Amount (Mass) of the hardness causing salt x 100)/ Molecular weight of hardness causing salt

## Slide 19
UNITS OF HARDNESS:
The 5 different units in which the hardness of water is expressed as given below-
(1) Parts per million (PPM): PPM is the number of parts of CaCO3 equivalent hardness per 106 parts of water.
i.e., 1 PPM = 1 part of CaCO3 equivalent hardness in 106 parts of water.

## Slide 20
(2) Milli grams Per Litre (mg/litre): mg/L is the number of milligrams of CaCO3 equivalent hardness present per litre of water.
i.e., 1 mg/L = 1 mg of CaCO3 equivalent hardness in 1L of water.
But 1 L water weighs = 1 kg of water
1 kg = 1000 gms = 1000 x 1000 mg = 106 mg
∴ 1 mg/L = 1mg of CaCO3 equivalent per 106 mg of water
= 1 part of CaCO3 equivalent per 106 parts of water
∴ 1 mg/L = 1 ppm

## Slide 21
(3) Degree Of Clarke (oCl): It is number of grains (1/7000 lb) of CaCO3 equivalent hardness per gallon (10 lb) of water.
(or) It is defined as the number of parts of CaCO3 equivalent hardness per 70,000 parts of water.
∴ 1 oCl = 1 grain of CaCO3 eq. hardness per gallon of water.
(or) 1 oCl = 1 part of CaCO3 eq. hardness per 70,000 parts of water
∴ 1 ppm = 0.07 oCl

## Slide 22
(4) Degree Of French (oFr): It is the number of parts of CaCO3 equivalent hardness per 105 parts of water.
1 oFr = 1 part of CaCO3 equivalent hardness per 105 parts of water
∴ 0.1 oFr = 1 ppm
Note: The hardness of water can be converted into all the four units by making use of the following interconversion formula-
1 ppm = 1mg/L = 0.07oCl = 0.1oFr
1 oCl = 1.43oFr = 14.3 ppm = 14.3 mg/L

## Slide 23
(5) Milliequivalent per Litre (meq/L): It is the number of milliequivalent of hardness present per litre of water.
1 meq/L= 1 meq of CaCO3 per litre of water
= 10-3 x 50 g of CaCO3 eq. of hardness per litre of water
= 50 mg of CaCO3 eq. of hardness per litre of water
= 50 mg/L of CaCO3 eq.
= 50 ppm
1 meq/L= 50 ppm

## Slide 24
PROBLEM:
A sample of water gives an analysis 13.6 mg/L of CaSO4 , 7.3 mg/L of Mg(HCO3)2 . Calculate the total hardness and permanent hardness.
Sol:
Total hardness= Temporary hardness + Permanent Hardness = 5 + 10 = 15 mg/L = 15 ppm
Permanent hardness = 10 ppm
Temporary hardness= 5 ppm
Salt | Quantity (mg/L) | M. Wt. | Multiplication Factor | Eq. of CaCO3 | Hardness
CaSO4 | 13.6 | 136 | 100/ 136 | 13.6 x (100/ 136)= 10 | P
Mg(HCO3)2 | 7.3 | 146 | 100/ 146 | 7.3 x (100/ 146)= 5 | T

## Slide 25
DETERMINATION OF HARDNESS OF WATER BY EDTA METHOD:-
This is a Complexometric titration method where Ethylenediamine tetraacetic acid (EDTA) is used.
EDTA forms complexes with different metal ions at different pH.
Calcium & Magnesium ions form complexes with EDTA at pH 9- 10.
To maintain the pH 9- 10 NH4Cl, NH4OH buffer solution is used.

## Slide 26
4. The disodium salt of EDTA is used for complexation.
5. An alcoholic solution of Eriochrome Black-T (EBT) is used as an indicator.
EDTA
EDTA disodium salt
Metal-EDTA complex

## Slide 27
BASIC PRINCIPLE:
When hard water comes in contact with EDTA, at pH 9- 10, the Ca+2 & Mg+2 forms stable, colourless complex with EDTA.
Ca+2 + EDTA + pH 9-10  Ca-EDTA
Mg+2 + EDTA + pH 9-10  Mg-EDTA

## Slide 28
Working:-
To the hard water sample, the alcoholic blue coloured EBT indicator is added along with the NH4Cl + NH4OH buffer (pH 9- 10) solution.
EBT forms an unstable wine-red complex with Ca+2 & Mg+2.
(Ca+2 + Mg+2) + EBT + Buffer (pH 9-10)  (Ca-EBT + Mg-EBT) complex
(Hard water) (Indicator) (Unstable wine-red complex)
This wine-red coloured [Ca-EBT & Mg-EBT] complex is then titrated against EDTA; when EDTA replaces EBT from Ca-EBT & Mg-EBT complex and forms stable colourless [Ca-EDTA] & [Mg-EDTA] complex releasing the blue coloured indicator EBT into H2O.
[Ca-EBT + Mg-EBT] complex + EDTA  EBT + [Ca-EDTA + Mg-EDTA] complex
(Unstable wine-red complex) (Blue) (Stable colourless complex)
Hence the colour change at the end point is wine-red to blue colour.

## Slide 29
The titration is carried out in the following steps 1. PREPARATION OF STANDARD HARD WATER: Dissolve 1gm of pure, dry CaCO3 in minimum quantity of dilute HCl and evaporate the solution to dryness on a water-bath. Dissolve the residue in distilled water to make 1 litre in a standard flask and shake well.
Molarity of standard hard water solution =
wt. of CaCO3 = 1 = 0.01M
M.wt. of CaCO3 100

## Slide 30
(2) PREPARATION OF EDTA SOLUTION:
Dissolve 4 gms of pure EDTA-disodium salt crystals along with 0.1 gm of MgCl2 in one litre of distilled water.
(3) PREPARATION OF INDICATOR (EBT):
Dissolve 0.5 gms of Erichrome Black-T in 100 ml of alcohol.
(4) PREPARATION OF BUFFER SOLUTION: Add 67.5 gm of NH4Cl to 570 ml of concentrated ammonia solution and dilute with distilled water to one litre

## Slide 31
(5) STANDARDISATION OF EDTA SOLUTION: Pipette out 20 ml of standard hard water solution into a conical flask. Add 2- 3 ml of buffer (pH 9- 10) solution and 2- 3 drops of EBT indicator. Titrate the wine-red coloured complex with EDTA taken in a burette after rinsing it with EDTA solution till the wine red colour changes to clear blue.
Note the burette reading and let the volume be “x”ml. Repeat the titration to get concurrent values.

## Slide 32
(6) TITRATION OF SAMPLE HARD WATER (Total) :
Pipette out 20 ml of the water sample into a 250ml conical flask, add 2- 3 ml of buffer (pH 9- 10) solution and 2- 3 drops of EBT indicator. Titrate the wine-red coloured solution with EDTA taken in the burette till a clear blue coloured end point is obtained.
Let the volume of EDTA be “y” ml. Repeat the titration to get concurrent values

## Slide 33
(7) TITRATION FOR PERMANENT HARDNESS:
Pipette out 100 ml of hard water sample in a beaker and boil till the volume reduces to 20 ml. All the bicarbonates of Ca++ and Mg++ decomposes to CaCO3 and Mg(OH)2. Cool the solution and filter the water into a flask, wash the beaker and precipitate with distilled water and add the washing to conical flask. Add 2- 3 ml of buffer (pH 9- 10) solution and 2- 3 drops of EBT indicator and titrate with EDTA solution taken in the burette till a clear blue colour end point is obtained.
Note the burette reading. Let the volume be “z” ml.

## Slide 34
CALCULATIONS:
Molarity of standard hard water solution = 0.01 M.
(Calculated in the preparation of standard hard water)
Molarity of EDTA solution (M2 ): V1M1 = V2M2
n1 n2
n1 & n2 are no. of moles of Ca+2 and EDTA = 1 each
i.e., n1=1, n2=1
V1 = volume of standard hard water
M1= Molarity of standard hard water
V2= volume of EDTA
M2= molarity of EDTA
M2 = V1M1 = 20 X 0.01
V2 x (titre value)

## Slide 35
Molarity of sample hard water (M3 ):
V2M2 = V3M3
n2 n3
V2= volume of EDTA
M2= molarity of EDTA
V3= volume of sample hard water
M3= Molarity of sample hard water
M3 = V2M2 = M2 x y (titre value)= y x 0.01
V3 20 x
Total Hardness Of Water
= M3 x 100 gms/1 litre
=M3 X 100 X 1000mg/L or ppm= (y/ x) X 1000ppm

## Slide 36
Permanent Hardness Of Water:
V2M2 = V4M4 M4= V2M2 = zM2 = z X 0.01
n2 n4 V4 20 x
V2= volume of EDTA
M2= molarity of EDTA
V4 = volume of water sample containing permanent hardness (100 ml)
M4= Molarity of water sample containing permanent hardness
Permanent Hardness Of The Water Sample
= M4 x 100 x 1000 ppm
= z/ x X 1000ppm

## Slide 37
Temporary Hardness Of The Water Sample
= (Total Hardness – Permanent Hardness)
= (M3 x 100 x1000 – M4 x 100 x1000) ppm
= (M3 – M4) x 100 x1000 ppm
= (y-z) X 1000 ppm
x

## Slide 38
Problem:
1 gm of CaCO3 was dissolved in HCl and the solution was made upto 1 Lit with distilled water. 50 ml of the above solution required 30 ml of EDTA solution for titration. 50 ml of hard water sample required 40 ml of the same solution of EDTA for titration. 50 ml of the hard water after boiling, filtering, etc. required 30 ml of the same EDTA solution for titration. Calculate the temporary hardness of the water.

## Slide 39
Soln:
Molarity of CaCO3 (SHW) solution (M1)= 1/100= 0.01 M Molarity of EDTA solution (M2 ) = V1 M1/ V2
V1= volume of CaCO3 solution = 50 ml
M1= Molarity of CaCO3 solution = 0.01 M
V2= volume of EDTA = 30 ml
M2= 50 x 0.01/ 30 = 0.016 M
Molarity of Hard Water Sample Sol.(M3 )= V2M2/ V3
V2= volume of EDTA = 40 ml
M2= Molarity of EDTA = 0.016 M
V3= volume of hard water sample= 50 ml
M3= 40 x 0.016/ 50 = 0.0128 M

## Slide 40
Total Hardness of water
= 0.0128 x 100 x 1000
= 1280 ppm
Permanent hardness of water: = V4 M4 = V2 M2
n4 n2
M4 = V2M2/ V4
n4=1; V2= volume of EDTA = 30 ml
n2=1; M2= molarity of EDTA = 0.016
V4= volume of permanent hardness containing water = 50
M4 = 30 x 0.016/ 50= 0.0096 M

## Slide 41
Permanent hardness of water
= 0.0096 x 100 x 1000 = 960 ppm
Temporary hardness
= Total hardness – Permanent hardness
= 1280 – 960 = 320 ppm

## Slide 42
20ml of SHW containing 1.2gm CaCO3 per litre required 35ml of EDTA. 50ml of hard water sample required 30ml of same EDTA. 100ml of hard water sample after boiling, cooling required 25ml of same EDTA. Calculate the hardness.
Solution: Strength of SHW= 1.2gm/ lit = 1200mg/ 1000ml = 1.2mg/ ml
Volume of SHW= 20ml = 20 x 1.2 = 24mg of CaCO3 eq hardness
Now, 20ml SHW = 35ml EDTA; i.e. 35ml EDTA = 24mg of CaCO3 eq hardness
So, 1 ml EDTA= 24/35 mg CaCO3 hardness
50ml WS = 30ml EDTA = 30 x 24/35 mg CaCO3 hardness= 20.57mg
Thus, 1 lit WS= 1000ml = 1000 x 20.57/50 = 411.4mg
So, Total hardness = 411.40ppm
100ml of boiled sample= 25ml EDTA = 25 x 24/35 = 17.14mg CaCO3 hardness
Thus, 1 lit BWS= 1000ml = 1000 x 17.14/100 = 171.4mg
So, Permanent hardness = 171.40ppm
Temporary Hardness = Total hardness – Permanent hardness
411.40 – 171.40 = 240.00ppm

## Slide 43
BOILER TROUBLES:
Water finds a great use in various industries for generation of steam in boilers. When water is continuously evaporated to generate steam, the concentration of the dissolved salts increase progressively causing bad effects for steam boilers. The following are the boiler troubles that arise:
Priming and foaming
Caustic embrittlement
Boiler corrosion
Scale and sludge formation

## Slide 44
PRIMING & FOAMING:
Priming: When a boiler is steaming rapidly, some particles of the liquid water are carried along with the steam. This process of “WET STEAM” formation is called ‘PRIMING’. Priming is caused by:
Presence of large amount of dissolved solids
High steam velocities
Sudden boiling
Improper boiler design
Sudden increase in steam production rate

## Slide 45
It can be avoided by: (Preventions)
Maintaining low water level
Using softened water
Fitting mechanical steam purifiers
Using a well-designed boiler
Avoiding rapid change in steam rate
Blow-down of the boiler

## Slide 46
FOAMING:
Foaming is phenomenon of formation of foam or bubbles on the surface of water inside the boiler with the result that the foam may pass along with the steam.
Causes: The presence of large quantity of suspended impurities and oils lowers the surface tension producing foam.
Preventions: Foaming can be avoided by-
Adding anti foaming chemicals like castor oil
Removing oil from boiler water by adding compounds like “NaAlO2 ”
Blow down of the boiler can prevent the foaming

## Slide 47
Disadvantages Of Priming & Foaming:
Priming & Foaming may cause the following boiler troubles:-
The actual height of the water in boiler is not judged
Wastage of heat with the result that it becomes difficult to keep up steam pressure and efficiency of the boiler is lowered

## Slide 48
CAUSTIC EMBRITTLEMENT:
Caustic embrittlement is a term used for the appearance of cracks inside the boiler particularly at those places which are under stress such as rivetted joints due to the high concentration of alkali leading to the failure of the boiler. The cracks have appearance of brittle fracture. Hence, the failure is called “Caustic Embrittlement”

## Slide 49
Reasons for the formation of Caustic Embrittlement:
The boiler feed water containing carbonates and bicarbonates of alkali metals, sodium hydroxide (NaOH) and a small quantity of silica or sodium silicate; it is purified by Lime-Soda Process.
During the softening process by lime soda process, free Na2CO3 is usually present in small portion in the soft water which decomposes to give NaOH and CO2 at high pressure of the boilers.
Na2CO3 + H2O  2NaOH + CO2
The precipitation of NaOH makes the boiler water “Caustic”
The NaOH containing water flows into the small pits and minute haircracks present on the inner walls of the boiler.
As the water evaporates, the concentration of caustic soda (NaOH) increases progressively, creating a “Concentration Cell”

## Slide 50
Thus, dissolving the iron of the boiler as Sodium Ferrate.
Fe + 2NaOH  Na2FeO2 + H2
The cracking of the boiler occurs particularly at stressed parts like bends, joints, rivets, etc. causing the failure of the boiler.
The iron at plane surfaces surrounded by dilute NaOH becomes Cathodic; while the Iron at bends, rivets and joints is surrounded by highly concentrated NaOH becomes Anodic which consequently decayed or corroded
(Anodic site) Conc NaoH || dil NaoH (Cathodic site)
Iron at Joints &bends Iron at Plane surface
Prevention Of Caustic Embrittlement:
By adding Na2SO4 , tannin, etc. to the boiler water which blocks hair cracks. There by preventing infiltration of caustic soda solution
By using sodium phosphate as the softening agent instead of sodium carbonate

## Slide 51
DISADVANTAGES OF CAUSTIC EMBRITLLEMENT:
The cracking or weakening of the boiler metal causes failure of the boiler
(3) BOILER CORROSION: The decay of boiler material by chemical/ electro- chemical attack by its environment is called “Boiler Corrosion”.
Reasons for boiler corrosion are: (a) Dissolved oxygen (b) Dissolved CO2 (c) Acids from dissolved salts.

## Slide 52
Dissolved Oxygen: Water usually contains about 8 mg/L of dissolved oxygen at room temperature. Dissolved O2 at high temperature attacks boiler material.
2Fe + 2H2O + O2  2Fe(OH)2↓ (ferrous hydroxide)
4Fe(OH)2↓ + O2  2[Fe2O3.2H2O]↓ (ferric oxide) Removal of dissolved O2 :
By adding calculated quantity of sodium sulphate (or) hydrazine (or) sodium sulphide
2Na2SO3 + O2  2Na2SO4
Sodium Sulphite
N2H4 + O2  N2 + 2H2O
Hydrazine
Na2S + 2O2  Na2SO4

## Slide 53
(b) Dissolved CO2:
Dissolved CO2 has slow corrosive effect on the materials of boiler plate. Source of CO2 into water is the boiler feed water which contains bicarbonates. Under the high temperature and pressure, maintained in the boiler the bicarbonates decompose to produce CO2.
Ca(HCO3 )2  CaCO3 + CO2 ↑ + H2O
Mg(HCO3 )2  Mg(OH)2 + 2CO2 ↑
The disadvantage of the CO2 is slow corrosive effect on boiler plates by producing carbonic acid
CO2 + H2O  H2CO3

## Slide 54
Removal of CO2:
By the addition of calculated quantity of ammonia.
2NH4OH + CO2  (NH4 )2CO3 + H2O
(c) Acids from dissolved salts:
Water containing dissolved Mg-salts liberate acids on hydrolysis
MgCl2 + 2H2O  Mg(OH)2↓ + 2HCl
Disadvantages of the acid production is that the acids react with Iron of the boiler plate in a chain reaction to produce decay of the metal.
Fe + 2HCl  FeCl2 + H2
FeCl2 + H2O  Fe(OH)2 + 2HCl
Fe(OH)2 + H2O + 1/2O2  Fe2O3 .3H2O (ferric oxide)

## Slide 55
Consequently even a small amount of MgCl2 can cause corrosion to a large extent.
Preventions:
Softening of boiler water to remove MgCl2 from the water
Addition of corrosion inhibitors like sodium silicates, sodium phosphate & sodium chromate
By frequent blow-down operation i.e., removal of water, concentrated with dissolved salts and feeding the boiler with fresh soft water.
Sludges and Scales formation: In boiler, water evaporates continuously and the concentration reaches saturation point, they form precipitates (scale or sludge) on the inner wall of the boiler

## Slide 56
SLUDGE: “Sludge is a soft, loose and slimy precipitate formed within the boiler”. Sludge are formed by substances which have greater solubility in hot water than in cold water. Salts like MgCO3 , MgSO4 , MgCl2 , CaCl2 etc., are responsible for sludge formation in boilers.
Disadvantages:
Sludge is a bad conductor of heat, hence it wastes a portion of heat generated.
Excessive sludge formation reduces the efficiency of the boiler.

## Slide 57
Prevention:
(a) Frequent blow-down operation should be carried out.
(b) Use well-softened water.
SCALES: “Scales are the hard, adhering ppt formed on the inner wall of the boiler”. Very difficult to remove once they are deposited on Inner wall of the boiler.
They formed due to decomposition of Calcium bicarbonate, Calcium sulphate etc..,
Ca(HCO3)2  CaCO3 ↓ + H2O + CO2 ↑

## Slide 58
REMOVAL OF SCALES:
Frequent blow-down operation can remove the scales which are loosely adhering.
By chemical treatment eg: CaCO3 scale removed by washing with 5-10% of HCl.
By giving thermal shocks.
Prevention: Use soft water.

## Slide 59
SOFTENING OF WATER:
The removal of hardness causing salts from water is called “Softening of water”.
The 3 Industrial methods employed for softening of water are:
Lime-Soda Process
Zeolite (or) Permutite Process
Ion-Exchange (or) Demineralization process

## Slide 60
LIME-SODA PROCESS:
This process is based on converting the soluble calcium and magnesium salts into Insoluble calcium carbonate and magnesium hydroxide precipitates by addition of calculated amount of lime (Ca(OH)2) and Soda (Na2CO3). The precipitate are removed by filtration. Any free dissolved CO2 and acids are also removed by this process. The various chemical reactions involved in this process are:

## Slide 61
For Calcium and Magnesium bicarbonates, only lime is required
Ca(HCO3)2 + Ca(OH)2  2CaCO3↓ + 2H2O
Mg(HCO3)2 + 2Ca(OH)2  2CaCO3↓ + Mg(OH)2↓ + 2H2O
(b) For MgSO4 & MgCl2 , both lime & soda are required
(iii) MgSO4 + Na2CO3 + Ca(OH)2  Mg(OH)2↓ + CaCO3↓ + Na2SO4
(iv) MgCl2 + Na2CO3 + Ca(OH)2  Mg(OH2)↓ + CaCO3 + 2NaCl
(c) For CaSO4 & CaCl2, only Soda is required
(v) CaSO4 + Na2CO3  CaCO3↓ + Na2SO4
(vi) CaCl2 + Na2CO3  CaCO3↓ + 2NaCl

## Slide 62
(d) Other Reactions: Free acids, CO2 , H2S dissolved iron and aluminium salts etc are also removed in this process
2HCl + Na2CO3  2NaCl + H2O + CO2↑
H2SO4 + Na2CO3  Na2SO4 + H2O + CO2↑
CO2 + Ca(OH)2  CaCO3↓ + H2O
H2S + Ca(OH)2  CaS↓ + 2H2O
FeSO4 + Ca(OH)2  Fe(OH)2↓ + CaSO4
Al2(SO4)3 + 3Ca(OH)2  2Al(OH)3↓ + 3CaSO4 + H2O

## Slide 63
Constituent | Reaction | Requirement
Ca+2 (Permanent) | CaSO4 + Na2CO3  CaCO3↓ + Na2SO4 CaCl2 + Na2CO3  CaCO3↓ + 2NaCl | S
Mg+2 (Permanent) | (iii) MgSO4 + Na2CO3 + Ca(OH)2  Mg(OH)2 ↓ + CaCO3↓ + Na2SO4 (iv) MgCl2 + Na2CO3 + Ca(OH)2  Mg(OH2 ) ↓ + CaCO3 + 2NaCl | L + S
HCO3- | (v) 2NaHCO3 + Ca(OH)2  CaCO3 + H2O + Na2CO3 | L - S
Ca(HCO3)2 (Temporary) | (vi) Ca(HCO3 )2 + Ca(OH)2  2CaCO3↓ + 2H2O | L
Mg(HCO3)2 (Temporary) | (vii) Mg(HCO3)2 + 2Ca(OH)2  2CaCO3↓ + Mg(OH)2↓ + 2H2O | 2L
CO2 | (viii) CO2 + Ca(OH)2  CaCO3↓ + H2O | L
H+ | (ix) 2HCl + Ca(OH)2 + Na2CO3  CaCO3 + 2NaCl + H2O | L + S
Coagulants FeSO4 | (x) FeSO4 + Ca(OH)2  Fe(OH)2 + CaSO4 2Fe(OH)2 + H2O + O2 2Fe(OH)3 CaSO4 + Na2CO3  CaCO3 + Na2SO4 | L + S
Al2(SO4)3 | (xi) Al2(SO4 )3 + 3Ca(OH)2  2Al(OH)3↓ + 3CaSO4 + H2O 3CaSO4 + 3Na2CO3  3CaCO3 + 3Na2SO4 | L + S
NaAlO2 | (xii) NaAlO2 + H2O  Al(OH)3 + NaOH | -L

## Slide 64
Calculation:
100 parts by mass of CaCO3 are equivalent to 74 parts of Ca(OH)2 and 106 parts of Na2CO3.
Amount of lime required for softening = 74/100 (Temp Ca2+ + 2 x Temp. Mg2+ + Perm. (Mg+2 + Fe+2 + Al3+) + CO2 + H+ (HCl/H2SO4 ) + HCO3 - all in terms of CaCO3 equivalent)
Amount of soda required for softening = 106/100 (Perm. (Ca2+ + Mg2+ + Fe+2 + Al3+) + H+ (HCl/H2SO4) + HCO3 - all in terms of CaCO3 eq.)

## Slide 65
COLD-LIME-SODA PROCESS:

## Slide 66
In this method the lime & soda are mixed with hard water at room temperature with constant stirring.
Generally the precipitates formed by this process are finely divided and in order to settle the precipitates, coagulants like alum, ferrous sulphate, etc. are added.
The hard water to be softened is mixed with calculated quantity of chemicals (Lime + Soda + Coagulant) from the top into the inner chamber on vigorous stirring. The chemical reactions takes place and the hardness producing salts get converted into insoluble precipitates.
The sludge is removed from the bottom of the outer chamber while the softened water passes through a wood fibre filter to ensure the complete removal of any residual sludge particles.
The clear softened water is withdrawn from the top of the outer chamber.
The softened water from this process contains a residual hardness of 50-60ppm

## Slide 67
HOT-LIME-SODA PROCESS:

## Slide 68
This process is similar to the cold lime-soda process, but no coagulant is needed.
Here the process is carried at a temperature of 80o to 150oC. Since the reaction carried out at high temperature.
(a) The reaction takes place faster
(b) The sludge settles rapidly
(c) Viscosity of soft water is lower, hence filtered easily
(d) The dissolved gases such as CO2, air, etc. driven out of the water
(e) The residual hardness is low, compared to cold lime- soda process.
Hot lime soda process consists of three parts-
“REACTION TANK” in which complete mixing of water, chemicals and steam takes place and water gets softened.
“Conical Sedimentation Vessel” where the sludge settle down.
“SAND FILTER” where sludge is completely removed.
The softened water from this process contains a residual hardness of 15-30 ppm.

## Slide 69
ADVANTAGES OF LIME-SODA PROCESS:
This process is economical.
Mineral content of the water is reduced.
The process increases the pH value of water, which reduces the content of pathogenic bacteria.
Manganese and Iron salts are also removed by this process.
The process improves the corrosion resistance of the water.
DISADVANTAGES OF LIME-SODA PROCESS:
Due to residual hardness, water is not useful for high pressure boilers.
Large amount of sludge is formed which create disposal problem.

## Slide 70
PROBLEMS:
Calculate the quantities of Lime & Soda required to soften 5000 litres of water containing the following salts: MgCl2 = 15.5 ppm; Ca(HCO3)2 = 32.5 ppm, CaSO4 = 22.4 ppm; Mg(HCO3)2 = 14.6 ppm; NaCl = 50 ppm
Soln: Calculation of Calcium Carbonate Equivalents:
Impurity mg/L | M. Wt. | CaCO3 eq. | Requirement
MgCl2 = 15.5 | 95 | 15.5 x 100 ÷ 95= 16.31 | L + S
Ca(HCO3)2 = 32.5 | 162 | 32.5 x 100 ÷ 162= 20.06 | L
CaSO4 = 22.4 | 136 | 22.4 x 100 ÷ 136= 16.47 | S
Mg(HCO3)2 = 14.6 | 146 | 14.6 x 100 ÷ 146= 10 | 2L
NaCl = 50 | - |  | 

## Slide 71
Lime = 74/100 (Temp Ca2+ + 2 x Temp. Mg2+ + Perm. (Mg+2 + Fe+2 + Al3+) + CO2 + H+ (HCl/H2SO4 ) + HCO3 - all in terms of CaCO3 equivalent) x (Vol of water/ 1000) x (100/ %P)
Lime required for litre of water:
= 74/100 (Ca(HCO3)2 + 2 x Mg(HCO3)2 + MgCl2) as CaCO3 eq.
= 74/100 (20.06 + 2x10 + 16.31)
= 74/100 x 56.37
= 41.71 mg
Lime req’d for 5000 litres of water
= 41.71 x 5000 ÷ 1000 = 208.55 g= 0.208 kg

## Slide 72
Soda = 106/100 (Perm. (Ca2+ + Mg2+ + Fe+2 + Al3+) + H+ (HCl/H2SO4) + HCO3 - all in terms of CaCO3 eq.) x (Vol of water/ 1000) x (100/ %P)
Soda req’d for litre of water
= 106/100 [MgCl2 + CaSO4] as CaCO3 eq.
= 106/100 [16.31 + 16.47]
= 106/100 [32.78]
= 34.74 mg
Soda req’d for 5000 litres of water:
= 34.74 x 5000 ÷ 1000 = 173.70 gm= 0.173 kg

## Slide 73
Zeolite or Permutit Process:
Zeolite is “Hydrated sodium alumino silicate”. Its general formula is: Na2O.Al2O3.xSiO2.yH2O; x= 2- 10 y= 2- 6. Eg: Natrolite: Na2O.Al2O3.3SiO2.2H2O.
Natural zeolites are generally non-porous.
The artificial zeolite is called Permutit. These are prepared by heating together with chain clay, feldspar and soda ash. These are porous and have greater softening capacity than natural zeolite.

## Slide 74
Working:
They exchange Na+ ions with the hardness, producing ions (Ca2+, Mg2+, etc.) in water.
Sodium Zeolite is denoted as Na2Ze.
PROCESS: In this process hard water is passed through a bed of zeolite at ordinary temperature. The hard water percolates (filtered), Ca+2, Mg2+ present in hard water are exchanged with Na+ ions. The following reactions taking place:
MgCl2 + Na2Ze  MgZe + 2NaCl
MgSO4 + Na2Ze  MgZe + Na2SO4
CaCl2 + Na2Ze  CaZe + 2NaCl

## Slide 75
CaSO4 + Na2Ze  CaZe + Na2SO4
Mg(HCO3)2 + Na2Ze  MgZe + 2NaHCO3
Ca(HCO3)2 + Na2Ze  CaZe + 2NaHCO3
Regeneration Of Zeolite: On continuous passing of hard water through sodium zeolite bed it is converted to calcium and magnesium zeolite which is known as ‘Exhausted Bed’. Hence, it must be regenerated. This can be done by washing zeolite bed with 10% sodium chloride solution.
CaZe + 2NaCl  Na2Ze + CaCl2
MgZe + 2NaCl  Na2Ze + MgCl2

## Slide 77
ADVANTAGES:
The equipment is small and easy to handle.
It requires less time for softening.
Water obtained from this process contains a residual hardness upto 10 ppm.
Easy to regenerate.
No sludge is formed in this process.
DISADVANTAGES:
Highly turbid water cannot be treated by this process.
The process exchanges only Ca+2 & Mg2+ ions by sodium ions and hence the softened water contains more sodium salts.
All the acidic ions like HCO3- , CO32-, etc. are not removed by this process.
Sodium bicarbonate decomposes in the boiler releasing CO2 which leads to corrosion.
While Na2CO3 is hydrolysed to NaOH which creates caustic embrittlement of boiler.

## Slide 78
Problem-1:
The hardness of 10,000 Lit of hard water was completely removed by passing it through a zeolite softner. The zeolite softner required 5000Lit of NaCl solution containing 1170mg/Lit. Determine the hardness of water sample.
Solution: 5000L of NaCl solution= 5000 x 1170mg/Lit
= 5850000mg
= 5850000 x 50 mg CaCO3 eq.
58.5
= 5000000mg
Hardness of 10000Lit water= 5000000mg
Thus, hardness for 1Lit= 5000000/ 10000 = 500mg CaCO3 eq
Hence, Hardness = 500ppm

## Slide 79
Problem-2:
An exhausted zeolite softner was regenerated by passing 75Lit of NaCl solution having strength 75g/Lit. If hardness of water is 300ppm, then calculate the total volume that can be softened by the zeolite.
Solution: Amount of NaCl in 75Lit= 75 x 75 = 5625gm of NaCl
Quantity of NaCl= 5625 x 100 = 4807.69gm= 4.81 x 106mg CaCO3 eq.
117
Hardness= 300ppm
So, 4.81 x 106 ppm is present in 4.81 x 106 Lit of water
300
= 1.6 x 104 Lit
Thus, Zeolite can soften 1.6 x 104 Lit of water

## Slide 80
ION EXCHANGE PROCESS/ DEMINERALISATION PROCESS:
Ion exchange resins are insoluble, cross-linked, long chain organic polymers.
The functional groups attached to the chains can exchange hardness producing cations and anions present in the water.
PROCESS: The process involves the following steps:
1) The first chamber is packed with cation exchange resin (RH+). When the hard water is passed through a bed of cation exchange resin it exchanges H+ with Ca+2, Mg+2, K+, Na+ etc. of hard water.
2RH+ + Mg+2Cl2  R2Mg2+ + 2H+Cl
2RH+ + Ca2+Cl2  R2Ca2+ + 2H+Cl
Thus, the hardness producing cations (Ca2+, Mg2+ etc) are removed

## Slide 81
1) The second chamber is packed with anion exchange resin. The water coming out of the first chamber contains H+, Cl-, SO42- and HCO3- ions.
It is now passed through anion exchange resin bed which can exchange OH- ions with anions like Cl-, SO42- and HCO3-
R-OH + Cl-  RCl + OH-
2R-OH + SO42-  R2SO4 + 2OH-
Thus, hardness producing anions like Cl-, SO42- and HCO3- are removed.
3) Thus, H+ ions produced from first chamber combine with OH- ions produced from second chamber to form water.
H+ + OH-  H2O
Hence, the water produced from ion-exchange process is completely free from all cations and anions of salts.

## Slide 84
REGENERATION OF RESINS:
The resin bed gets exhausted, when used for a long period and can be regenerated:
(a) The exhausted cation exchange resin can be regenerated by passing dil. HCl (H+)
R2Mg2+ + 2H+  2RH+ + Mg2+
R2Ca2+ + 2H+  2RH+ + Ca2+
(b) The exhausted anion exchange resin can be regenerated by passing dil. NaOH (OH-)
RCl + OH-  ROH + Cl-
R2SO4 + 2OH-  2ROH + SO42-

## Slide 85
ADVANTAGES:
1) The softened water by this method is completely free from all salts and fit for use in boilers.
2) It produces very low hardness nearly 2 ppm.
3) Highly acidic or alkaline water can be treated by this process.
DISADVANTAGES:
1) The equipment is costly.
2) More expensive chemicals are required for regeneration.
3) Turbid water cannot be treated by this method.

## Slide 86
Numerical
After treating 104 litres of water by ion-exchange, the cationic resin required 200 litres of 0.1N HCl and the anionic resin required 200 litres of 0.1N NaOH solutions for regeneration. Find the hardness of water.
Solution: Hardness of 104 litres of water= 200lit of 0.1N HCl
= 200 x 0.1 Lit x 1 N CaCO3 eq.
= 20 lit of 1N CaCO3 eq.
= 20 x 50 g of CaCO3 eq.
= 1000 g of CaCO3 eq.
So, Hardness in 1lit water= 1000/ 104 g of CaCO3 eq.
= 100 mg of CaCO3 eq.
Thus, hardness of water sample= 100ppm